This call registers a mouse subsystem within a session.
##### Syntax
MouRegister (ModuleName, EntryName, Mask)
##### Parameters
;ModuleName (PSZ) - input : Address of the dynamic link module name. The maximum length is 9 bytes (including ASCIIZ terminator). ;EntryName (PSZ) - input : Address of the dynamic link entry point name of a routine that receives control when any of the registered functions are called. The maximum length is 33 bytes (including ASCIIZ terminator). ;Mask (ULONG) - input : A mask of bits, where each bit set to 1 identifies a mouse function being registered.
##### Return Code
;rc (USHORT) - return:Return code descriptions are: * 0 NO_ERROR *385 ERROR_MOUSE_NO_DEVICE *413 ERROR_MOUSE_INVALID_ASCIIZ *414 ERROR_MOUSE_INVALID_MASK *415 ERROR_MOUSE_REGISTER *466 ERROR_MOU_DETACHED *505 ERROR_MOU_EXTENDED_SG
##### Remarks
The Base Mouse Subsystem is the default mouse subsystem. There can be only one MouRegister outstanding for each session without an intervening MouDeRegister. MouDeRegister must be issued by the same process that issued MouRegister.
When any registered function is called, control is routed to EntryName. When this routine is entered, four additional values are pushed onto the stack. The first is the index number (Word) of the function being called. The second is a near pointer (Word). The third is the caller's DS register (Word). The fourth is the return address (DWord) to the mouse router. For example, if MouGetNumMickeys were called and control routed to EntryName, the stack would appear as if the following instructions were executed: PUSH@ WORD NumberOfMickeys PUSH WORD DeviceHandle CALL FAR MouGetNumMickeys PUSH WORD Function Code CALL NEAR Entry point in Mouse Router PUSH DS CALL FAR EntryName. When a registered function returns to the Mouse Router, AX is interpreted as follows: AX = 0 No error. Do not invoke the Base Mouse Subsystem routine. Return AX = 0. AX = -1 Invoke the BaseMouse Subsystem routine. Return AX = return code from the Base Mouse Subsystem. AX = error (if not 0 or -1) Do not invoke the Base Mouse Subsystem Routine. Return AX = error. When the mouse router receives a mouse call, it routes it to the Base Mouse Subsystem unless an application or other mouse subsystem has previously issued MouRegister for that call. If the call was registered, the subsystem is entered at the EntryName specified, and provided with the applicable function code.
The registered function mask is used to determine whether a requested function is performed by the registered mouse subsystem or default to the Base Mouse Subsystem.
The following list shows the relationship of the mouse API calls and the Function Code passed to either the Base Mouse Subsystem or a registered mouse subsystem. {|class=“wikitable” !MOU API calls||Function Code||Function Mask
MouGetNumButtons		00H

MouGetNumMickeys		01H

MouGetDevStatus		02H

MouGetNumQueEl		03H

MouReadEventQue		04H

MouGetScaleFact		05H

MouGetEventMask		06H

MouSetScaleFact		07H

MouSetEventMask		08H

MouGetHotKey		09H

MouSetHotKey		0AH

MouOpen		0BH

MouClose		0CH

MouGetPtrShape		0DH

MouSetPtrShape		0EH

MouDrawPtr		0FH

MouRemovePtr		10H

MouGetPtrPos		11H

MouSetPtrPos		12H

MouInitReal		13H

MouFlushQue		14H

MouSetDevStatus		15H

A registered mouse sybsystem must leave the stack, on exit, in the exact state it was received.
##### Bindings
#### C
<PRE> #define INCL_MOU
USHORT rc = MouRegister(ModuleName, EntryName, Mask);
PSZ ModuleName; /* Module Name */ PSZ EntryName; /* Entry Name */ ULONG Mask; /* Function Mask */
USHORT rc; /* return code */ </PRE>
#### MASM
<PRE> EXTRN MouRegister:FAR INCL_MOU EQU 1
PUSH@ ASCIIZ ModuleName ;Module Name PUSH@ ASCIIZ EntryName ;Entry Name PUSH DWORD Mask ;Function Mask CALL MouRegister
Returns WORD </PRE>
##### Related Functions
* MouDeRegister
Mou