This call obtains a DBCS (double byte character set) environmental vector that resides in the country information file.
##### Syntax
DosGetDBCSEv (Length, Country, MemoryBuffer)
##### Parameters
;Length (USHORT) - input : Length, in bytes, of the data area (MemoryBuffer). This value should be at least 10. ;Country (PCOUNTRYCODE) - input : Address of the country information structure: countrycode (USHORT)
Country code identifier. 0 is the default country code.
codepage (USHORT)
Code page identifier. 0 is the code page of the current process.
; MemoryBuffer (PCHAR) - output : Address of the country dependent information for the DBCS environmental vector. This memory area is provided by the caller. The size of the area is provided by the input parameter Length. If it is too small to hold all the available information, then as much information as possible is provided in the available space.
The format of the information returned in this buffer is: Word Description 1 First range definition for DBCS lead byte values
      High byte Binary start value (inclusive) for range one
      Low byte Binary stop value (inclusive) for range one.
2 Second range definition
      High byte Binary start value for range two
      Low byte Binary stop value for range two.
N Nth range definition
      High byte Binary start value for Nth range
      Low byte Binary stop value for Nth range.
N + 1 Two bytes of binary 0 terminate list.
      For example:
       DB 81H,9FH DB E0H,FCH
       DB 00H,00H
##### Return
rc (USHORT) - return
Return code descriptions are: * NO_ERROR * 396 ERROR_NLS_NO_COUNTRY_FILE * 397 ERROR_NLS_OPEN_FAILED * 398 ERROR_NO_COUNTRY_OR_CODEPAGE * 399 ERROR_NLS_TABLE_TRUNCATED
##### Remarks
The returned DBCS environmental vector may be for the default country and current process code page or for a specific country and code page. For more information on code page see DosSetCp.
##### C Binding
<PRE> typedef struct _COUNTRYCODE { /* ctryc */
USHORT country; /* country code */
USHORT codepage; /* code page */
} COUNTRYCODE;
#define INCL_DOSNLS
USHORT rc = DosGetDBCSEv(Length, Structure, MemoryBuffer);
USHORT Length; /* Length of data area provided */ PCOUNTRYCODE Structure; /* Input data structure */ PCHAR MemoryBuffer; /* DBCS environmental vector (returned) *
USHORT rc; /* return code */ </PRE>
##### MASM Binding
<PRE> COUNTRYCODE struc
ctryc_country dw ? ;country code
ctryc_codepage dw ? ;code page
COUNTRYCODE ends
EXTRN DosGetDBCSEv:FAR INCL_DOSNLS EQU 1
PUSH WORD Length ;Length of data area provided PUSH@ OTHER Structure ;Input data structure PUSH@ OTHER MemoryBuffer ;DBCS environmental vector (returned) CALL DosGetDBCSEv
Returns WORD </PRE>
# Note
Text based on http://www.edm2.com/index.php/DosGetDBCSEv
Family API
DOS	Process Manager	DosBeep DosExit DosSleep DosExecPgm
File Manager	DosChDir DosChgFilePtr DosClose DosDelete DosDupHandle DosMkDir DosMove DosQCurDir DosQCurDisk DosSetFileMode DosOpen DosQFileInfo DosRead DosQFileMode DosQFSInfo DosQVerify DosRmDir DosSelectDisk DosFindClose DosFindFirst DosFindNext DosSetFileInfo DosSetVerify DosWrite DosFileLocks DosSetFHandState DosNewSize DosBufReset DosQFHandState DosSetFSinfo
Memory Manager	DosFreeSeg DosSubAlloc DosSubFree DosSubSet DosAllocHuge DosAllocSeg DosReallocHuge DosReallocSeg DosGetHugeShift DosCreateCSAlias
NLS	DosCaseMap DosGetCtryInfo DosGetDBCSEv DosSetCtryCode DosGetCollate DosGetMessage DosInsMessage DosPutMessage
Date and Time	DosSetDateTime DosGetDateTime
Devices	DosDevConfig DosDevIOCtl DosDevIOCtl2
Signals	DosHoldSignal DosSetSigHandler
Misc	BadDynLink DosGetEnv DosGetMachineMode DosGetVersion DosError DosErrClass DosSetVec
KBD		KbdCharIn KbdFlushBuffer KbdGetStatus KbdSetStatus KbdStringIn KbdPeek
VIO		VioGetBuf VioGetConfig VioGetCurPos VioGetCurType VioGetPhysBuf VioReadCellStr VioReadCharStr VioScrollUp VioScrollDn VioScrollLf VioScrollRt VioScrUnLock VioSetCurPos VioSetCurType VioSetMode VioGetMode VioShowBuf VioWrtCellStr VioWrtCharStr VioWrtCharStrAtt VioWrtNAttr VioWrtNCell VioWrtNChar VioWrtTTY VioScrLock VioPopUp
Tools		BIND
Modules		DOSCALLS.DLL VIOCALLS.DLL KBDCALLS.DLL MSG.DLL
Libraries		API.LIB OS2386.LIB FAPI.LIB DOSCALLS.LIB SUBCALLS.LIB